## Slide 1: Origins Space Telescope (OST) Mission Concept Overview
Instrument Interface and Face-to-Face Meetings
Science and Technology Definition Team (STDT)
A. Flores, Mission Systems Engineer (MSE)
NASA Goddard Space Flight Center
8800 Greenbelt Road, Greenbelt, MD 20771
June 13, 14 & 15, 2017

## Slide 2: GSFC Design Team Members
OST GSFC Design Team Members are as follows:
  Study Scientist: David “Dave” Leisawitz
  Deputy Study Scientist: Johannes Staguhn
  Study Manager (401): Ruth Carter
  System Architect/Technologist (542): Mike DiPirro
  Mission Systems Engineer (MSE) (599): Anel Flores
  Instrument System Engineer (ISE) (592): James “Jim” Kellogg and Ed Amatucci
  Optics (551): Joe Howard and James Corsetti
  Cyro (541): Ed Canavan
  Mechanical (543):, Greg Martin and Andrew Jones
  Thermal (545): Lou Fantano
  ACS (591): Eric Stoneking
  Flight Dynamics: Dave Folta and Casandra “Cassie” Webster
  Propulsion: Daniel “Dan” Rampspacker
  Electromechanical (544): Rajeev Sharma
  Structural Analysis and Modelling (542): Tim Carnahan
  Materials (541) : Carley Sandin, Kevin Hodges
  Detectors (553): Kevin Denis
  Electrical and Data Systems (564): Damon Bradley and Porfirio Beltran
  Integration and Test (568): Susanna Petro
  Mission Operations & Ground System (581): Steve Tompkins

## Slide 3: OST Mission Goals
The Origins Space Telescope is the mission concept for the Far Infrared Surveyor, a study in development by NASA in preparation for the 2020 Astronomy and Astrophysics Decadal Survey
OST is planned to be a large aperture (8-m to 15-m), actively-cooled telescope (~4K) covering a wide span of the mid- to far-infrared spectrum. Its spectrographs with enable three-dimensional surveys of the sky that will discover and characterize the most distant galaxies, exoplanets and the outer reaches of our Solar System. The observatory is planned to be placed in the Sun-Earth L2, similar to JWST.
Principal Science Themes include:
Tracing the Signatures of Life and the Ingredients of Habitable Worlds
Unveiling the Growth of Black Holes and Galaxies over Cosmic Time
Charting the Rise of Metals, Dust, and the First Galaxies
Characterizing Small Bodies in the Solar System
Measuring exoplanet biosignatures to search for signs of life

## Slide 4: Top-Level Mission Requirements
Observatory to Accommodate the following five (5) instruments:
  Medium Resolution Survey Spectrometer (MRRS) – JPL
  Hi Res (Far-IR) Spectrometer (HRS) - GSFC
  Heterodyne Instrument (HI) – Europe
  FIR Imager/ Polarimeter (FIP) – GSFC
  MID-IR Imager Spectrometer/ Coronagraph (MISC) – JAXA
Instrument Wavelength Coverage: 6 to 600 microns
Mission Duration: 5 years nominal with up to 10 years extended
Baseline Observatory to fit into a 5-m launch vehicle fairing, because this fairing size is rather common and is expected to be available for the foreseeable future.
Telescope size: the largest telescope compatible with a launch in a 5 m fairing, with the understanding that it’s aperture would be approximately 9 meters in diameter
Telescope type: three mirror, unobstructed, off-axis field
Observatory will be placed in appropriate orbit to be able to conduct the required science observations
Observatory operating temperature: 4 to 4.5 K
Observing Strategies: under development, TBD
Appropriate launch vehicle to place the observatory in the proper orbit
Observatory will transmit the science data to the Earth Mission and Science Operations Center’s (MOC and SOC)
Serviceable observatory: the instruments will be designed in serviceable modules with grapples and fixtures for servicing. A modular design could be helpful in I&T due to the accessibility of the instruments. We will assume the propellant fuel will also be serviceable. A servicing mission for OST itself; however, is not required to be designed at this stage.

## Slide 5: Top-Level Derived Requirements
Orbit: Sun-Earth L2
Mission Classification: Class A, generally fully redundant and cross strapped
Launch Vehicle (LV): Vulcan Aces, Falcon Heavy or similar LV capability
LV Fairing Size: 5-m Atlas V fairing or similar
Launch Date: Mid-2030’s
Optical Telescope Assembly (OTA) Temperature: 4 K Actively cooled using cryocoolers
Baseline non-articulating (i.e., fixed) telescope: articulation could be considered if it is required by the science requirements. However, an articulating telescope will require a gimbal mechanism, which has to be cold. Such a mechanism will add complexity, cost and risk.
Instruments to be designed with appropriate internal redundancy and Level 1 components.
Instrument electronics will be separate, located in the spacecraft bus (warm side), from the cold portion of the instruments located in the Instrument Accommodation Module (IAM) behind the OTA on the cold side of the observatory
OST will provide ~4K for the instruments and an intermediate ~20 K zone for readout electronics using a total of eight cyro-coolers.
The instruments will have to share a total 100 milli-watts on the telescope cold-side not necessarily equally.
Total observatory power required is TBD watts at BOL.
Consumables: such as propellant fuel, will be sized for 10 years
OST will attempt to achieve attitude control requirements similar to JWST (or a combination with WFIRST) if possible, although, these requirements will be revised when all of the instruments requirements are known.

## Slide 6: OST Instrument Optical Inputs Summary
Yellow cells highlight telescope design drivers

## Slide 7: Notional Unobstructed, Off-Axis Field, Observatory
Actively cooled (~4K) Baffle Assembly
(not shown on right, see inset below for concept)
Incident light
9.1-m Aperture Diameter Primary Mirror (~4 k), Three mirror, unobstructed, off-axis field
Sunshield
Five (5) Layers*
0.75-m Spacing
Fixed (Deployable, Non-articulating) Optical Telescope Element (OTE)
Cold Side
(Inner Layer
~35K)
Warm Side
(250 – 300K)
Deployed Observatory Configuration
+X
+Z
+Y
Sun
*Assumes parallel spacing between layers. Angular spacing between the Sunshield layers is also being explored
Field of Regard
+5˚ to -45˚ Pitch off Sun line
±180˚ Yaw about Sun line
±5˚ Roll about Line of Sight (LOS)

## Slide 8: Unobstructed Observatory Aft View
Notional Radiator
Notional Solar Array
High Gain Antenna (HGA) (Behind Radiator)
Spacecraft bus
Outermost Sunshield Layer
Field of Regard
-5˚ to -45˚ Pitch off Sun line
±180˚ Yaw about Sun line
±5˚ Roll about Line of Sight (LOS)
Deployable Tower Assembly (DTA)
(segmented)

## Slide 9: Unobstructed Observatory Side Views Showing Light Trace
Light Ray Trace
Instrument Accommodation Module (IAM)
Deployable Tower Assembly (DTA), Segmented
4.4m
Primary Mirror (PM)
PM to attach to IAM with a two-Axis Gimbal (TBD)

## Slide 10: Unobstructed Observatory Top-View
Dimensions in Meters
25.7m
14.8m

## Slide 11
Instrument Accommodation Module (IAM)
FIP
MRSS
MISC
HRS Ray Trace (in green)
HI
HI Ray Trace (in blue)
Telescope Focal Surface
HRS
Cut-Away View showing Instruments

## Slide 12
HI & HRS Instrument Ray Traces in the IAM and IAM Top-view
IAM Top-view
HI Ray Trace
IAM Aft-View Looking FWD
HRS Instrument & Its Ray Trace
FIP

## Slide 13: Observatory ROM Mass Estimate
Instrument and Flight System masses are preliminary and relatively immature

## Slide 14: OST Instrument and Accommodation Requirements

## Slide 15: Instrument Attitude Control System Questionnaire Responses

## Slide 16: Attitude Control System
Driving Requirements
  Absolute Pointing: 44 mas (MISC)
  Onboard Pointing Knowledge: 30 mas (MRSS Inertial Point)
  Jitter: 22 mas RMS (MISC)
  Scanning Rate: 100 arcsec/sec (MRSS Large Survey)
Assumptions
  Moments of Inertia: [120,000 170,000 100,000] kg-m^2
    2x JWST (till we know better)
  Momentum Accumulation 450 Nms/day
    At 45-deg pitch
    “Compact” sunshield
    Total specular reflection
    Mass center assumed [3.0 0.0 4.0] from sunshield major fold center
    Looking into techniques for reducing accumulation rate
      Tailor sunshield reflectivity?
      Trim tab?
Solar Radiation Torque Vs. Pitch

## Slide 17: OST Optical Performance Budget

## Slide 18: Future Work and Trades
Complete initial OTE design inclusive of deployment, in particular. As its design progresses determine its structural frequency is adequate in the deployed configuration.
Complete IAM and Spacecraft bus initial designs.
Define concept packaging and deployment schemes for the Sunshield and Baffle Assembly
Complete initial designs for the Deployable Tower Assembly (DTA) and the IAM’s hinge mechanism. Resolve whether the DTA needs to be located or partially located inside of the spacecraft bus.
Explore angular spacing between Sunshield layers.
Commence a Structural, Thermal, Optics, and Pointing (STOP) analysis.
Determine observatory Center of Pressure and Center of Gravity for stability.
Single or dual axis solar array gimbal trade.

## Slide 19: Issues and Concerns
Packing of the telescope assembly remains a challenge in order to get everything to fit within the 5-m fairing. Total observatory volume, mass and power remain concerns.
The OTE areal mass is very preliminary and is assumed to be ~40 kg/m2. JWST’s OTE areal density is ~68 kg/m2.

## Slide 20: Acronyms
  Con Ops – Concept of Operations
  DTA – Deployable Tower Assembly
  FIP – Far Infrared Imager/ Polarimeter
  FOV – Field of View
  HGA – High Gain Antenna
  HI - Heterodyne Instrument
  HRS - High Resolution (Far-IR) Spectrometer
  IAM - Instrument Accommodation Module
  ISE – Instrument Systems Engineer
  JWST – James Webb Space Telescope
  LOS – Line of Sight or Loss of Signal
  MISC - MID-IR Imager Spectrometer/ Coronagraph
  MCWG – Mission Concept Working Group
  MOC – Mission Operations Center
  MRSS - Medium Resolution Survey Spectrometer
  MSE – Mission Systems Engineer
  OST – Origins Space Telescope
  OTE – Optical Telescope Element
  PM – Primary Mirror
  SOC – Science Operations Center
  STDT – Science and Technology Definition Team
  STOP - Structural, Thermal, Optics, and Pointing analysis
  WFIRST – Wide Filed Infrared Survey Telescope

## Slide 21: Back-up Slides
Unobstructed Observatory Side Views Showing the Spacecraft Bus
Areal Density for JWST
Aft View of the Instrument Accommodation Module (IAM)
MRSS and HI Instrument Volumes

## Slide 22: Unobstructed Observatory Side Views Showing the Spacecraft Bus
+X
+X
+Z
+Z
HGA located behind radiator

## Slide 23: Areal Density for JWST

## Slide 24: IAM Top-View Without Aft IAM Hosuing

## Slide 25: Telescope Field of View (FOV) Layout