## Slide 1
Science Requirements vs observing time trades

## Slide 2: Core Community Surveys – Observing time trades
Relationship between science requirements and observation time for each survey is complex because there are multiple ways to adjust observation time for each survey
In what follows, we’ll list the survey parameters that affect observing time, and describe the impact of changing them

## Slide 3: High Latitude Wide Area Survey - Imaging
Reduction in Survey Area
  Reduces statistical power of survey
  Reduces sensitivity to largest angular scales
  Reduces margin in budget that could be available to devote to other terms
Reduction in Survey Depth
  Reduces statistical power of survey by reducing the number of galaxies
    Loss is preferentially at higher redshifts
  Reduced sensitivity on small angular scales
  Reduced precision of PSF characterization affects entire sample
  Several planned internal calibrations may be degraded

## Slide 4: High Latitude Wide Area Survey - Imaging
Reduce number of dithers
  Reduced sampling PSF (Roman pixels are undersampled at 0.11 arcsec)
    Because chip gaps cause parts of survey to have fewer exposures than the rest, these areas are already at the minimum number of samples
  Increases effects of chip gaps on survey depth
    Already have significant variation in cumulative exposure time over survey area
Reduce number of filters
  Would impact ability to determine photo-z over significant redshift ranges
  Reduces ability to detect subtle wavelength-dependent PSF errors
  Would reduce ability to use cross-power spectrum tests of shear bias
    Shear maps in 3 filters provides internal consistency checks and test for multiplicative bias

## Slide 5: High Latitude Time Domain Survey
Reduce Survey Area
  Number of transients
  Loss is greater than linear as smaller tiling pattern is less efficient: lose increasing fractions of light curve as tiling pattern rotates on the sky
Increased Cadence
  Ability to characterize SNIa
  Coarse sampling of light curve reduces accuracy of light curve fits at low redshift end of sample
Reduced Imaging Exposure time
  Number of transients as a function of redshift
  Ability to characterize transients
  Reduces accuracy of SNIa luminosity distance determination
Reduced Prism Exposure times
  Redshifts, classification, standardization, systematics and evolution control
Reduced Number of filters
  Broad wavelength range to measure colors and build templates
  Greatly reduced SNIa redshift coverage in each tier

## Slide 6: Galactic Bulge Time Domain
Reducing time allocation to this program does not affect:
    Survey Area
    Cadence
    Imaging Exposure time
    Number of filters
  Because the survey revisits the same fields over and over at a particular cadence
  Conversely: don’t save time by changing any of the above
Reducing duration of seasons:
  Reduces number of planets,
  more than linearly because light curves are interrupted, especially for gaps in the middle of a season
Reducing Number of Seasons
  Reduces number of planets

## Slide 7: Trade Space for High Latitude Survey
Current HLWA survey will enable galaxy shape measurements in multiple colors and two roll angle
  Provides exquisite control of systematics
To reach the weak lensing FoM requirement in minimum time, could survey part of the Rubin footprint with a single wide-band filter (Euclid-like)
  Good statistical constraining power for weak lensing
  BUT
    Won’t provide internal checks on shear systematics for the region with a single NIR filter
    No color information in near IR, degraded photo-z at z>1
    Meets the letter, but not the spirit of objective 1 (wide field IR survey to AB 26.5 mag)
      Greatly impacts astrophysics science return

## Slide 8: Backup

## Slide 9: Survey Capability Requirements Summary
1: Mass function for
1MEarth< m <30Mjupiter
to <15%
2: Mass function for
0.1MEarth< m <0.3MEarth
to <25%
3: masses, distances
to 40% host stars
4: free-floating
planet frequency
5: estimate ηEarth
Exoplanet Microlensing
(EML 2.0.x)
1: FoMSN>325
2: μ(z), 0.2≤ z ≤ 1.7
σμ ≤ 0.02
per Δz=0.1
3: >100 SNIa
per Δz=0.1
4: σz /(1 + z) bias
Supernova Cosmology
(SN 2.0.x)
1: FoMBAO>7533
2: FoMRSD>4047
3: Slitless spectra
4: Completeness
> 0.6
5: redshift accuracy,
outlier fraction
Galaxy Redshift
(HLSS 2.0.x)
1: FoMWL>327400
2: Neff>27/arcmin2
3: Additive shear
error <2.7 10-4
4: Multiplicative shear
bias <3.2 10-4
5: deep field
Weak Lensing
(HLIS 2.0.x)

## Slide 10: Key Wide Field Science Performance Requirements
Representative values shown; full details in SRD. |  | Expansion, Structure, NIR Survey |  | Expansion | Exoplanet
 |  | Weak Lensing | Galaxy Redshift Survey | Supernovae | Microlensing
Surveys & Data | Area/Survey Speed | 0.20 deg2/hr (1,700 deg2) | 0.34 deg2/hr (1,700 deg2) | 14, 5 deg2 >100 SNe/Δz=0.1 | 586 deg2-day Over 6+ seasons
 | Redshift | 0≤z≤3 | 1.1 < z < 1.9 (2.9 w/OIII) | 0.2≤z≤1.7 | 
 | Sensitivity | S/N≥18 @ 24.4/24.3/23.7 (AB J/H/F184) reff=0.18” | S/N≥6.5 for 1.0x10-16 erg/cm2/s | S/N≥13 (brightest filters at peak) | S/N>100 for HAB=21.4 star
 | Cadence |  |  | ~ 5 days | 15 min
 | Data Vol. | ≥3 reads/exp | ≥3 reads/exp | ≥3 reads/exp | ≥3 reads/exp
PSF | Quality | EE50 ≤ 0.12” (J) EE50 ≤ 0.17” (IFC) | EE50≤0.21”@1.5 mm | EE50 ≤ 0.12” (J) EE50 ≤ 0.14” (IFC) | EE50 ≤ 0.15” (wide)
 | Stability | 1 nm RMS 𝚫WFE in 180s |  |  | 
 | Knowledge | 2nd moment ≤7.2x10-4 Ellipticity ≤5.7x10-4 |  | 0.2% | 
Flux Calibration Relative Over | Time | 0.5% /observing program | <2% rel spect-photometry | <0.5% / 2 wk | <0.1%/season
 | Wavelength | <2% abs/0.5% photo zeropt | <2% rel over bandpass | <2% abs/ 0.5% photo zeropt | <3% abs <1.4% photo zeropt
 | Dynamic Range |  |  | <0.3% 15<AB<26 | <0.1% over 2 mag
 | Area | <10 mmag | <2% rel over survey area |  | 
Color | Filters | 4 NIR bands for photo-z, 3 reddest for shapes | Overlap with HLIS for 3 filter imaging | 6 filters 0.5-2.0mm | Wide filter, & 1 short, 1 longward of 1mm
 | Dispersion |  | 10-12 Å/pix | 70 < R < 150 |